## Slide 1: On the Robotic Uncertainty of Fully Autonomous Traffic
LI, Hangyu
hangyu.li@connect.ust.hk
Advised by Dr. SUN, Xiaotong
CTS2022 August 15-16
Intelligent Transportation Thrust
Systems Hub, HKUST(GZ)

## Slide 2
Contents
Introduction
Model
  Scenario statement
  Safety evaluation
  Average collision-inclusive capacity
Discussion
  Influence of parameters
  Suggested control on variables
  Generalization of the model
Conclusion
2

## Slide 3
1. Introduction
3
AVs offer the potential to improve both traffic safety and efficiency.
Human Driven Vehicles:
Accidents caused by human errors (main cause of car crashes)
Congestion propagation due to the heterogeneity of driver intentions
Autonomous Vehicles (assumed):
Intelligent decision-making abilities
Accurate machinery operations
Shorter stable headway
Increased roadway capacity

## Slide 4
1. Introduction
4
Perception
Localization
Planning
Control
AVs
with
ERROR
AVs

## Slide 5
1. Introduction
5
Uncertainty
Lack of laws and rules
Public concerns
Focus on safety but sacrifice efficiency
Perception algorithms
Fusion localization
Control strategies
Ensure stability but neglect traffic benefits
Development
Validation

## Slide 6
1. Introduction
6
Fully autonomous traffic
OUR MODEL
Collision Probability
Car-following Scenario
Collision-inclusive
capacity
Rear-end
collision rate
Two-state stochastic process
Normal
Blocked

## Slide 7
2. Model - Scenario
7
Forward perception – only follow the certain car in front
Longitudinal control – only acceleration and braking are considered
Rear-end collision – consider single-lane one-time rear-end collisions as the only source of capacity reduction
Predetermined speed – view speed as an exogenous variable independent of traffic density
Ideal road section – Independent section has no bottleneck at the downstream

## Slide 8
2. Model – Car following with perceptual error
8
Newell’s model:
with perceptual error:

## Slide 9
2. Model – Error propagation
9
When ego vehicle (e) follows
the front stochastic vehicle (f)
with observation error (o)
When randomness stabilizes,
stochasticity of each vehicle converges
and
distance (d) becomes time-invariant

## Slide 10
2. Model – Safety measurement
10
Safe Region
Collision
Region
Front Vehicle
Supposed Position
Possible Positions

## Slide 11
2. Model – Collision-inclusive capacity
11
Collision
Clearance
Normal
Blocked (duration of TCT)
Transitions
(normal capacity)
(zero capacity)
(reduced flow per collision)

## Slide 12
2. Model – Collision-inclusive capacity
12
Total Clearance Time (TCT)
Collision-inclusive capacity
expected number of collisions
reduced flow per collision

## Slide 13
3. Discussion – Parameters
13
Length of a vehicle ()
Safety (-) Capacity (-)  Compact vehicles may be more favored.
Precision of observation()
Safety (+) Capacity (+)  More precise sensors lead to safer traffic and thereby contributing to greater traffic capacity and overall benefit.
Time step ()*
  Contribution to headway. (Could be neglected for general values.)
  Number of updates of a discrete system. Negative to capacity sorely but allow larger .
Size of sliding window ()*
  Contribution to headway. (Could be neglected for general values.)
  Error propagation from perception to motion. Positive to both safety and capacity but reduces sensitivity in dynamic scenes.
* See our latest paper for more details.

## Slide 14
3. Discussion – Suggested control on variables
14
* See our latest paper for proof and more details.
Set capacity as the goal of optimization:
Two-stage: controlled by single vehicle and decided by the platoon.
Derivative:
(*) For most of cases, decreases first and then increases. The only solution to exists and serves as the optimal .

## Slide 15
3. Discussion – Suggested control on variables
15
* See our latest paper for proof and more details.
Set capacity as the goal of optimization:
Two-stage: controlled by single vehicle and decided by the platoon.
(*) As long as a exists, monotonically decreases. The original capacity function’s monotonically increasing suggests that driving as fast as possible only when under reasonable limits by road conditions, such as the curvature, slope, unevenness, etc.

## Slide 16
3. Discussion – Suggested control on variables
16
Optimal control on headway
General suggested control

## Slide 17
3. Discussion – Generalization
17
From Car-following to other scenarios
error propagation
(Localization)
(Decision-making)
(Position with uncertainty)
safety measurement
collision-inclusive capacity
As long as AV systems and the traffic environment are modeled,
safety performance and collision-inclusive capacity could be analytically derived.

## Slide 18
4. Conclusion
18
Model
Robotic error: from perception to position uncertainty, leading to possible collisions
Safety: integrated collision probability
Capacity: average collision-inclusive capacity reduced by collision blocks
Discussion
Parameters: simple with vehicle length and perception precision, but complex with time step and size of sliding window
Optimal control: locally optimal control on headway, and monotone relationship with speed
Generalization: from the simple car-following to more general scenarios
Future plan
Consider more realistic high-order models to include random acceleration and speed;
Reveal the perceptual error in practice and validate the model by experiments;
Conduct optimization with goals and constraints of realistic meanings based on our model.

## Slide 19
Thank you
for your attention
LI, Hangyu
hangyu.li@connect.ust.hk
Advised by Dr. SUN, Xiaotong
CTS2022 August 15-16
Intelligent Transportation Thrust
Systems Hub, HKUST(GZ)